Dear Customers:

Thanks for your trust and support! We will be happy to provide you with comprehensive service and technical support.

This manual will instruct you how to call API function package in CD-ROM before you using UHF series reader, and enable your software integration communicating with the reader, configuring reader parameters, controlling the reader to operate on tag and acquire tag returned operation information.

Please send your comments and suggestions about our products after using our products. We will always be attentive to your services.

This manual is suitable for the following readers:

The manual is supposed that the user already owns basic RFID and computer knowledge, so that related terms such as RFID, RF and Ethernet is not described in details, the users can search and inquire reference, or consult our technical department.

There are some signs with the following definitions:

Warning

If violate the signed operation method or usage environment, which will do damage to health or devices.

Advice

It will come to better effect according to the signed method.

tABLE OF CONTENTS

CHAPTER 1  Reader Introduction	1

1 . Reader Introduction	1

2 Technical Parameter	1

3 Reader Functionality	2

3.1  System Function	2

3.2  Tag Operation Function	4

CHAPTER 2  Reader Structure and Interface	5

1 Reader Structure	5

2 Reader Interface Specification	5

CHAPTER 3  Installation and Debugging	7

1 Installation Preparation	8

2 Installation Methods	8

2.1  Fixing Reader	8

2.2  Connection Components	9

2.3  Reader Parameter Configuration	11

3 Control Reader Operations	12

3.1  Call API Function Package	12

3.2  Transmit Data Stream	12

CHAPTER 4  Routine Maintenance and Repair	13

1 Common fault analysis and solve method	13

CHAPTER 5  RFID Integration Application	17

1 Application Assembly Explanation	17

1.1  Computer	17

1.2  Application Software	17

1.3  Communication Cable	18

2 Integration Application Reference	18

2.1  Signal Disturbance Issue	18

2.2  RF Signal Attenuation /Reflex	19

2.3  Optimization Method	19

3 Special Remind	20

3.1  The damage to human body	20

3.2  Disturbance by other devices	21

3.3  Application in special situation	21

CHAPTER 6  Transportation and Storage	22

1 Transportation Requirements	22

2 Storage Requirements	22

CHAPTER 7  Packaging and Accessory	23

1 Product Packaging	23

2 Accessories	23

CHAPTER 8  After Sales Service	24

After Sale Service	24

CHAPTER 1
Reader Introduction

## . Reader Introduction

Reader is R&D by our company specially for reading/writing tags of ISO18000-6B and ISO18000-6C (EPC Class1 Gen2) protocols. The reader has good characteristics, such as reliable, friendly operation, strong function, and flexible expandability, which is applied widely in logistics control, transportation management, asset management and production line management etc.

Reader provides multiple communication interfaces, including RS232 and Ethernet.

## Technical Parameter

Reader technical parameters as following:

Table 1-1：Reader technical parameters

| Technical Parameter | Explanation |
| --- | --- |
| Working Frequency | 860-960MHz, frequency band adjustable |
| Tag Protocol | ISO18000-6B, ISO18000-6C(EPC Class1 Gen2) |
| F. H. Mode | FHSS or fixed frequency |
| Frequency Points | 16 points (frequency points adjustable) |
| Wireless Data Speed | 40kbps |
| Antenna | Built-in circular antenna: 8dBi |
| Modulation Mode | ASK |
| Power Output | +20dBm~ +30dBm @50Ω load, step in 1dB |
| Reading Range | 0~8m |
| Writing Range | 0~3m |
| Interfaces | RS-232 interface, 10M/100M adaptive Ethernet port |
| Firmware Upgrade | Support serial port upgrade |
| Status Indicators | Built-in buzzer, power/antenna/tag reading/communication indicators |
| Power Supply | External power adaptor(150~20/50Hz AC input, DC 12V/3A output) |
| Power Consumption | 2W(standby), 10W(working) |
| Dimension | 250mm × 250mm × 76.5mm (L×W×H) |
| Weight | <2.0Kg |
| IP rating | IP55 |
| Operating Temperature | -40℃~60℃ |
| Storage Temperature | -60℃~80℃ |
| Humidity | 5%~95%(non-condensing) |

Operating frequency: The frequency of readers are related to local restrictions of UHF bands. Please confirm whether the frequency of readers comply to local frequency, i.e. China frequency band (920~925Mhz), Europe frequency band (865~868Mhz), North America frequency band (902~928Mhz), Japan frequency band (952~954Mhz), etc.

## Reader Functionality

This section explains the functions and characters of ..

### 3.1  System Function

- Multiple Communication Interfaces

. reader provides multiple communication interfaces catering for different application environments:

─  Standard RS-232 serial port, support speed range 9600~115200bps

─  Standard 10M /100M Base-T Ethernet interface, support AUOTO-MIX function, identify cross-line or straight line and automatically switches send/receive channels.

- Status Indicator

. reader provides the following status indicators: power, antenna selection and antenna port carrier output, reading tag, data communication indications. At the same time, it is equipped with buzzer to indicate reader operation status.

- Reader Name Configuration

User can set different name for each reader, and the set name could be stored and queried. Through this function, user can fast and easily find the connection established readers in different places, other than using IP address or label sticker to distinguish readers. This can also establish user-friendly database management.

- Antenna Port Disable and Enable

The built-in antenna of . can be configured as either enabled or disabled.

When host computer is using a forbidden antenna port to operate, the reader would reject and return error code. In order to prevent a port without antenna operating, this would result in error operation or even damage to devices.

- Independent Antenna Port Power Configuration

The antenna port of . reader could be set with different power output parameter.

- Modify Ethernet Configuration Parameter In Real-time

After modify the Ethernet configuration parameters of reader such as IP address, the reader would simultaneously update the parameter. It doesn't need restart or re-power.

When using the Ethernet connection to modify Ethernet configuration parameters, the reader will use the original Ethernet configuration parameters to maintain connection and communication, until the current connection is cut off. The reader Ethernet configuration is immediately updated when it is cut off, and the host computer will use new Ethernet configuration parameters to establish connection with reader.

When using other connecting methods to modify the Ethernet configuration parameters, the Ethernet configuration parameters will be updated immediately.

- Adaptive Reading Time

When a reader is continuously operating on tags, use the interval reading mode to reduce power consumption and to decrease interference with other devices. . reader will automatically adjust the interval according to actual working status. When there's no tag within RF environment, it will auto-adjust to standby monitoring status and increase the interval; when detected tags within the RF range, the interval will be reduced. Through this way, the power consumption and tag operation efficiency is achieved.

### 3.2  Tag Operation Function

- Tag Filtering

Reader can be configured to support the label filtering. After start the tag filtering function, if reader gets a tag ID and sends to host computer successfully, within the configured time reader would filter the same tag ID, and it will send the tag ID again when the configured time out. This feature can reduce the duplication of the tag information on the network congestion and control computer data processing burden.

This function has two parameters can be configured:

1)  Filtering startup and shutdown;

2)  Filtering time configuration, range from 100 milliseconds to 2 minutes.

- ISO18000-6B Tag Function

Reader can read tags which are compatible with ISO18000-6B protocol, and read UID code of ISO18000-6B tags, read/write data bank data, lock and lock status query.

- ISO18000-6C Tag Function

Reader can read tags which are compatible with ISO18000-6C protocol, and read EPC code of ISO18000-6C tags, read/write data bank data, lock and unlock.

- EPC Length Adaptive

The EPC code length of ISO18000-6C protocol tag is changeable, and . can read/write EPC code of different length.

- TID Length Adaptive

The TID code of ISO18000-6C tag is 8bytes, while many tag manufacturers keep TID code blank or only 4bytes. . can read TID code of different length.

CHAPTER 2
Reader Structure and Interface

This chapter explains the structure, external interface type and function definitions of . reader in details.

## Reader Structure

Integrated reader surface structure is showing as figure 2-1.

Figure 2-1 Reader Structure and Dimension

## Reader Interface Specification

Integrated reader has power port and communication interfaces, realizing power supply and communication function with computer or control equipment. The front panel interfaces figure as 2-2.

Figure 2-2  Reader front panel interfaces

Interface Definition:

“1”－ Ethernet interface, standard RF-45, with network status indicator

Yellow: Ethernet interface connection is normal;

Green: Flashing indicates Ethernet interface is sending and receiving data

“2”－ RS-232 interface, standard DB9(female type) interface block. Pin number, signal name and signal flow of identification are as following (Pin number and DB9 socket marked with the same number):

Table 2-1  DB9 Interface pin marks

| Pin Number | Signal Name | Signal Flow |
| --- | --- | --- |
| 2 | RXD | RS-232 data input |
| 3 | TXD | RS-232 data output |
| 5 | Gnd | Grounding |

“3”－ DC power input port, adapts XS-12 type standard aerial connector.

CHAPTER 3
Installation and Debugging

Please read this chapter carefully before installation and debugging.

To ensure your personal & property security and equipment running well, before installing, do the following preparations:

- Understanding of local power supply parameters; check the whether the voltage and frequency range comply with local power line.

Under some circumstance, due to electrical load or other reasons, voltage range may be greater volatility, understand the working environment carefully and the actual working state of power supply voltage before using.

- Please use the three-phase power socket and ensure a good grounding!

- For an outdoor environment, the installing location of reader should be rain, moisture and sun proof, well-ventilated.

- The reader must be pre-tested for proper installation.

- Before installation, measure the distance between reader and components (such as between reader and antenna, reader and computer, reader and power plug), to buy cable and plan system reasonably.

- Note the transmission distance limitations and type of the serial cable / USB cable / network cable (straight line, cross line); If you use a relay device, please note that the actual total length of the relay equipment and delay of data transmission.

- Check the working environment of reader and tag whether there are some factors existing between reader and tags, such as some large metal objects blocking or reflecting.

- Carefully analyze the work electromagnetic environment of working place before installation, and check whether there are some special restrictions on wireless equipments (such as hospital, airport). Knowing what are the devices working range within 900~960MHz (such as GSM base station), in order to reasonably configure the frequency and power of reader, if necessary it is recommended to use additional filtering components. If user has no sufficient experience at this, please feel free to contact supplier or its agent.

- When installing several readers under the same environment, please take care of the fixing methods and minimum distance between readers, the frequency configuration to avoid interfering.

## Installation Preparation

Before installing reader, please check the intactness of product function and completeness of files carefully. If there is any damage or shortage, please contact local supplier for replacement. Except for these, check whether the reader complies with the following installation conditions:

1) Meet the requirements of working environment (power and RF environment);

2) The tested reader working normal, interfaces in good condition;

3) The accessories are complete, and reach the required standard to fulfill a complete read/write application environment.

## Installation Methods

The appropriate installation methods mainly depend on its location. Usually, the readers are installed on the points where are safe and convenient for operation.

Antenna installation should try to avoid pointing to prolonged personal staying location.

### 2.1  Fixing Reader

According to the working environment, there are two types of installing, hanging and mounting, to meet different applications. In real application, people can combine the two methods for better reading performances. Figure 3-1

Figure 3-1  Reader installation drawing

### 2.2  Connection Components

This section will illustrate the connection method between reader, PC and power.

1)  Connecting Computer or Control Equipment

Reader has RS-232 and Ethernet two types of interfaces.

- Serial Port: The serial port is used for short distance connection (less than 5m), which can directly connect with computer through special cable.

There is one 1.5m RS-232 data cable in reader accessories. The connection of data cable is as following: figure 3-2

.                                     PC

Figure 3-2  RS-232 connection of data cable

- Ethernet port: Ethernet is used for long distance connection (10m), through reticle to connect switch (exchange) or hub. It can also connect directly with PC TCP/IP interface.

The reader can auto-identify crosswire and through straight wire, hence user can use any of the cables to connect computer or switch equipments.

2)  Power Adapter

Figure 3-3  Reader has packaged with specialized power adaptor.

Following the steps to power on reader:

1)  Please confirm the power and frequency from electric outlet meets the standard: AC150~240V/50Hz;

2)  Plug one end of the power cable to the power adaptor AC input port, and the other end to AC power outlet. The power indicator turns on.

3)  Plug the power adaptor DC output port into reader power input port;

The interface of reader uses aerial connector, with high reliability, easy to plug in/out. The following are pictures showing how to connect & disconnect.

4)  The following are pictures showing how to connect & disconnect.

Figure 3-4  Power plug in diagram

Hold the back-end of plug, after correctly pointing to the socket and push in. If you hear a crack, the plug is in and locked.

Figure 3-5 Power separation diagram

After holding tight the metal cover, and pull the plug out.

5)  After the reader is powered on, it will initial and self-detect the system. After the initialization, the buzzer in reader would sound three short beeps. All the indicators would light for one second, and then only power indicator is on. The whole process of initialization is completed and the reader is standby.

If the reader self-detects failed, the buzzer would sound 5 short beeps.

### 2.3  Reader Parameter Configuration

If the reader is used for the first time, you need to configure parameters. There are two methods:

1)  By calling API functions through their integrated software, users can configure system parameters.

2)  Through reader management software to configure system parameters.

There is a "Reader Software Manager" in accessory to control reader. Please refer to <800 Series Reader Management Software Instructions.pdf>.

## Control Reader Operations

The reader is a control equipment of command, which will execute operations only when receives instructions from computer or controlling equipment. There are two work methods for reader.

### 3.1  Call API Function Package

By calling API functions through their integrated software, users can configure parameters of reader and tag. Please refer to the <800 Series Reader API Programming Manual> for details.

### 3.2  Transmit Data Stream

In integration software, send data stream directly to achieve reader configuration and tag operations as the controlling protocol. Frame format and command definition of data stream, please refer to <RFID Reader Data Stream Controlling Protocol>. (This protocol is not included in CD unless it is required.)

CHAPTER 4
Routine Maintenance and Repair

This chapter is used to introduce the problem may encounter when using . and the simple fault diagnosis method.

If the consumer has problem or doubt in self -software control, please use the "reader management software" for test to confirm whether it is caused by software or by the reader.The configuration of the "reader management software"and the demo function have almost cover all the consumer functions.You can ask supplier Technical support for fictional realization.

## Common fault analysis and solve method

1) After switch on power light is not bright

- Check whether the 220V AC plug is with power.

- Check whether the adapter is normally connected with the plug, if it is ok power supply indicator will light green.

- Check whether the adapter connects the plug tightly. Please do as section 3.2 described, pull and insert the plug again. If there are any other readers, please use other adapter to test.

- Check whether the input AC voltage is in 150V～240V range.

- Check whether there are any high-power devices working around.

- Except the power light other lights is on. This is a hardware issue. Please pull out the power supply and contact supplier or agent for maintenance.

2)  After power on and connect the serial port line, run the management software failed.

- Check whether the serial port line is connected tightly. It's suggested to reconnect the serial port line with computer again.

- Check whether using the line from the accessories. If not, please check whether the line can satisfy the requirement described in section 3.2.2. Following the method: Use the multimeter to test whether pin 2 is conducted with pin 3; similarly, test whether pin 3 is conducted with pin 2; and test whether both ends of pin 5 is connected.

- Check whether there are multi-serial ports on computer or controller, and make sure software choose the correct port number as actual using.

- Check the Baud rate. Make sure the software the same Baud rate as the reader configuration. You can get the Baud rate in the "communication parameters" interface. After enter into the interface, double click the "Serial port speed detection" to get the Baud rate.

- Windows system has monopolized in serial port using. Please check whether other software is using the serial port.

- Check whether the serial port is breakdown. You change anther serial port in other PC to test or use other devices to test the serial port.

- If PC one side is using the "USB serial port" device, the drive of the device may be incompatible with API software. Especially for the device has installed the reader USB drive.

- You can check the reader function by USB or Ethernet connection.

3)  After power on and connect the Ethernet, run the management software failed.

- Check whether the Ethernet line is connected tightly. It's suggested to reconnect the Ethernet line with computer again;

- Check whether Ethernet line is in good condition: Use other Ethernet device or reticle test tool for test.

- The reader has "AUTO-MIX" function, it can auto identify the TX/RX data line and auto switchover send-receive access. But some accident may happen to cause identification fault (Such as disturbance by the over length of the reticle). It's suggested to use the right connect way. Use the direct-through line between reader router and concentrator. Use cross reticle between the reader and PC.

- The reader support "ping" functions. User can use the "ping xxx.xxx.xxx.xxx –t" to test the connection between reader and the network. "xxx.xxx.xxx.xxx" is the reader IP address.

- Make sure the PC and the reader have the matched Ethernet configuration, it means IP address share the same subnet mask in the same segment. You can check the Ethernet configuration by USB or serial connection.

- Check whether the fire wall settings in PC and related router, ADSL modem can shield the reader management software application, shield the SOCKET port. If yes, please use other port or open it. The default port is: 7086. You can change it in reader management software.

4)   Enter system parameter configuration interface, pointing out "system parameter inquire fail"

- Check the connection problem between the PC and the reader. Such as the break or fetch way of the serial port line, USB date line.

- Check whether the reader works smoothly. If necessary you can reboot the reader.

5)  Execute "Read EPC Code" function, the demonstrate software can not receive EPC code.

- Check whether the antenna light on panel of the Reader becomes red. If it is red, the reader has executed the ''Read EPC code operation". Please check the fault in the following ways. If it is still green, it explains that there are problems in the communication between the reader and PC, or the data cable connection. Please double check the default as described above.

- Check whether the antenna number selected in software is the same value with the PF antenna port actually using.

- Check whether using the linearly polarized antenna. If it is, please rotate 90 degree and then test.

- Check the plane of tag is parallel with the plane of antenna. Because most antennae need parallel position for good long-distance Reading ability. Vertical position is not allowed.

- Make sure whether the tag is intact. Change another ISO18000-6 tag for testing.

- Make sure whether the tag is ISO18000-6C（EPC Class1 Gen2）Tag.

- Make sure the tag number set in the software is matched with the tag number actually using. If it is too small than actually using, Read failure and slow speed will be caused by the large collisions.

6)  Execute "TID" function; demo software can not receive the TID code of the tag.

Please handle it as showing in the Section 5.

7)  Execute "TID" Function, "Read User Data Bank", function etc; demo software can not get TID code of the tag or reading failure.

- First please execute "Read EPC code" function. And then make sure whether Read EPC code is successful. If it can not, please check as showing in the section 5. If it can, check in the following ways.

- There may be no TID data bank in some tag, but our readers have good compatibility in handling this. But it can not guarantee all conditions. Please contact supplier to get details about the Tag parameters.

8)  Execute "Write EPC Code" function, "Read User Data Bank", "Change Destroy password", "Tag lock operation" function etc; demo software prompt failure.

- First please execute "Read EPC Code" function. And then make sure whether reading EPC code is successful. If it is not, please check as showing in the section 5.If it is successful, check in the following ways.

- There might be no user data bank in some tags, reader have good compatibility in handling this. But it can not guarantee all conditions. Please contact supplier to get details about the tag parameters.

- Tag write distance range is usually just 70% of maximum allowed distance. Please cut off the distance to confirm this factor.

CHAPTER 5
RFID Integration Application

## Application Assembly Explanation

A whole RFID integration application system is consist of reader, RFID tag, antenna, computer system and software. Please refer to the specific requirements of components as following:

### 1.1  Computer

Computer system is used to run the consumer system integration software. So it should at least satisfy the basic requirement for running the system integration software. Besides the integration system will use API function provided by supplier and it might be used to run the "Reader management software". So following the basic requirements:

1)  CPU PIII 600MHz, Memory 128M, Hard Disk more than10G.

2)  At least has one of RS-232 serial port or Ethernet interface

3)  With Windows 98/2000/XP Simplified or English operating system.

### 1.2  Application Software

The reader is attached with the following software:

1)  API DLL

Consumer can realize operation on the reader by call the DLL file, such as reader configuration, tag operation etc. Please check the detail method in the accessory optical disk file<800 series reader API programming reference manual>.

2)  Reader Management Software

This software is used to configure the system parameters. It can also be used to demonstrate the reader performance and functions, such as read Tag.

### 1.3  Communication Cable

. can communicate with computer in two basic ways: Ethernet port and RS-232 port. The requirements for Ethernet and RS-232 cables are as following.

Ethernet reticle: It's suggested to use standard Cat-5 lines and take standard RJ-45 joint. The reader can support AUTO-MIX function for reticle identification. It supports automatic identification in both direct-through line and crosswire. And the total length should no more than 100 meters.

Serial port cable: It's suggested to use standard serial port line. And the line with the standard DB9 (male and female) is crosswire. And the total length should no more than 5 meters.

## Integration Application Reference

RFID reader belongs to wireless communication device, which has a great relationship between the system performance and signal disturbance and attenuation. The section will give some advice about the reader optimizing usage.

### 2.1 Signal Disturbance Issue

Signal disturbance means when the reader and RFID Tag exchanging information, there are other RF signal or disturbance signal coming from other communication devices, strength of which to a fixed range around the tag working frequency range. The signal disturbance can badly decrease the capacity of the reader to read RFID tag data.

Interference signal source may come from the following way:

- Other RF system, the major it the wireless device work in 800MHz-1GHz range, such as 900M GSM base station, RPT.

- Remote control device, communication device or other device sending RF signal.

- RF radiation from huge electromechanical equipment.

All these factors can be eliminated or reduce by change the reader and antenna diction or add extra filter.

### 2.2  RF Signal Attenuation /Reflex

RF signal attenuation means the intensity of RF signal is nature decay in the air with distance increasing. It also means the attenuation caused by obstacle in the transmission path.

Because this device works in UHF frequency, small attenuation and poor diffraction capacity is the feature of the wireless signal. So the wood material (such as packing box) in the transmission path can cause great attenuation.

The rain can also cause great attenuation, so the rain, dense fog weather should be fully taken into consideration.

Almost every object (furniture or cut off) can cause attenuation in some degree. So it need to carefully adjust the antenna installation position to minimize the attenuation.

Signal reflex means wireless signal reflex when transmitted in the space encounter with another medium (metal, liquid) .Reflex from the RFID Tag back metal or metallized plane can also affect the signal quality. In some condition, this effect can enlarge the reading distance, meanwhile it can get a dead angle in the reading range.。When the RFID tag locates in these dead angles, the communication between the tag and the reader will very bad.

The possibility obstacle way for RF signal transmission is as following:

- Sealed space includes concrete wall, floor or ceiling.

- Metal plates which are around the antenna, such as electromechanical devices, irony furniture.

- Water or other liquid surrounds the antenna or tag.

Some kind of reflex seems to enlarge the reading distance, but it is not reliable and continuous. So we should not depend on this kind of increasing distance, or it will cause tag reading instability.

### 2.3  Optimization Method

General speaking, it's hard to make accurate forecast about reader system performance at random (because electromagnetic radiation is so complicated to handle, including signal frequency stability, direction map of the antenna and antenna side lobe issue, surrounding condition etc). Every RFID integrated system can get the optimal performance only after reality testing and debugging on spot. But, the following advice is meaningful in optimizing the system in most application environment.

- Carefully plan and install the reader.

- Environmental RF features including architectural space, building materials, around huge device and metal frame work, should be taken fully consideration. The difference of the RF features can both reduce and enhance the Reader working performance.

- In integration application it should not always pursue the working distance. Over-length can cause reading tag failure, especially in multi-Reader work condition.

- In integration application it should not always increase the power, theoretically, when the power enhance 16 times the reading distance can just increase 1 time. So it's more effective in optimizing the system.

- The direction of polarization of the antenna has a great effect on the reading distance. And it should be consistent with a direction of polarization of the RFID tag (Tag is always linear polarization).

- When the direction of polarization of the reader antenna is circular polarization, RIID tag can rotate 360 degree in the same plane with the reader without affecting the reading distance.

- Make sure the object containing RFID Tag for identification should stay in the effective reading range for more than 10ms.

- To avoid the disturbance caused by the multi-tag in the same object, there should have enough distance between the two RFID tags.

- Never make the Naked Tag without packaging to contact with chemicals. Some chemical, such as alcohol, has no effect to the Tag in room temperature but when temperature is higher it will has corrosiveness to the Tag.

## Special Remind

### 3.1  The damage to human body

The design of . can satisfy the National requirement about wireless device damage to human body. But in actual integration application, user should not stay in the Reader RF range for a long time.

### 3.2  Disturbance by other devices

The reader works in UHF frequency range. There are other working frequency ranges around, such GSM communication, broadcasting equipment. So before integration application, please check what kind of devices working in the UHF frequency range and make a detailed planning to avoid the disturbance to other devices also prevent the Reader be disturbed by other devices.

### 3.3  Application in special situation

There are special requirements about wireless device in hospital and airport. So if you want to use RFID application in these conditions, please do check the limitation about wireless devices. It's strongly suggested professional wireless test expert should take part in also professional test equipment should be used to test the signal frequency and strength. Or you can contact our technical departments for advice and assist.

CHAPTER 6 Transportation and Storage

## Transportation Requirements

The design and packaging of reader can satisfy the requirement of common electronic devices in road, railway, aviation, water transport.

## Storage Requirements

The long-term storage house for reader should be provided the following conditions:

- Ambient temperature: 40~+80℃；

- Relative humidity: No more than 80％(No condensation)；

- Ambient air without salt, acidity etc harmful gas.

CHAPTER 7
Packaging and Accessory

## Product Packaging

With internal anti-shock material box packaging can use large IBC for transportation.

## Accessories

Including principal machine, the packaging box also contains the necessary accessories and spare parts. Please check details in the following table.

Table 7-1 Product packaging box list

| Serial Number | Name | Unit | Quantity | Remarks |
| --- | --- | --- | --- | --- |
| 1 | Reader | pcs | one |  |
| 2 | 12V/3A Power adapter | pcs | one |  |
| 3 | Standard Ethernet reticle | pcs | one | 3m |
| 4 | RS-232 Cable | pcs | one | 2m |
| 5 | Installation Bracket | pcs | one |  |
| 6 | Installation Bolt | pcs | four |  |
| 7 | CD-ROM | pcs | one |  |
| 8 | Product warranty card | pcs | one |  |
| 9 | QC card | pcs | one |  |

Please seriously check the product and accessories according to product packaging box list in the manual. If it is inconsistent or there has any damage, please contact our company in time.

For further store and transportation, it is strongly suggested that all the packaging material should be preserved after opening the packaging.

CHAPTER 8
 After Sales Service

## After Sale Service

If user confronts with hard problems, please contact our technical support department for help.

Before contact our technical support department, please confirm and take down the following information for better communication:

Reader Information: Take down the reader model and serial no. on nameplate. If the management software can still communicate with reader, please write down the system configuration of reader in system config interface.

Integrated Application Information: Such as the conditions of installation, antenna type in use, the tag type, the application software and computer configuration, and so on…

# Text boxes

Version：V2. 0.0

### Integrated Mid-Range Reader User Manual

User Manual

版本：V2.0.0