Programming Manual

UHF Series Reader

Version: V2.0.0

Dear Customers:

Thanks for your trust and support! We will be happy to provide you with comprehensive service and technical support.

This manual will instruct you how to call API function package in CD-ROM when you using the UHF series reader and enable your software integration communicating with the reader, configuring reader parameters, controlling the reader to operate on tag and acquire tag returned operation information.

If you experience problems during operation, please contact our technical support department.

Your comments & suggestions are warmly welcome during your operation on our products. We will be always at your side.

This manual is suitable for the following readers:

UHF Series Reader

When this manual is written it is supposed that readers have basic knowledge over RFID and computer. The technical words, such as RFID, Radio Frequency & Ethernet etc. in this manual, are not specifically introduced. Please refer to other reference books or consult our technical department for support.

The following marks would appear in our manual, the meaning are as below:

Warning

If it disobey the restricted operations or using environments, it might be harm to human health or damage equipments.

Advice

Follow the advised instructions, the results might be better.

Table of Contents

Part I	Overview	1

1.	API Function Package Introduction	1

2.	API Function Description	1

Part II	Call of API	2

1.	Environment Requirements	2

2.	File Included	2

3.	API Call Methods	2

Part III	Special Explanation	3

1.	About Tag	3

1.1 EPC Tag	3

1.2 ISO8000-6B Tag	3

2.	About Reader	4

2.1 Antenna Port	4

2.2 Multi Reader	4

Part IV	API Function List	6

1.	Communication Control Function	6

2.	System Parameter Configuration Function	6

3.	Reader Operation Function	7

4.	Tag Operation Function	7

5.	API Configuration Function	8

Part V	API Function Description	9

1.	Communication Control Function	9

1.1  TCP Parameter Initialization	9

1.2  COM Port Parameter Initialization	9

1.3  USB Parameter Initialization	9

1.4  UDP Parameter Initialization	10

1.5  Establish Connection	10

1.6  Close the Connection	10

1.7  Re-connect reader	10

1.8  Check the connection	10

2.	Configuration of System Information	11

2.1  System Information Setting	11

2.2  Query of System Information	11

2.3  Configuration of Working Mode	11

2.4  Operation on System Parameter List	12

2.5  Configuration of Carrier	12

2.6  Query Carrier Parameter	12

2.7  Configuration of Communication Parameter	13

2.8  Query Communication Parameter	13

2.9  Configuration of Network Parameter	13

2.10  Query Network Parameter	14

2.11  Configuration of Tag Operation Parameter	14

2.12  Query Tag Operation Parameter	14

2.13  Configuration of Expansion Board Parameter	15

2.14  Query Expansion Board Parameter	15

2.15  Query RF Port Parameter	15

2.16  Query Specified RF port Parameter	16

2.17  Configuration of RF port parameter	16

2.18  Specified RF port Enable Configuration	17

2.19  Specified RF port Power Configuration	17

2.20  Specified RF port Cycling Query Configuration.	18

3.	Reader Operation Functions	18

3.1  Stop Reading	18

3.2  Carrier Operation	18

3.3  IO Output Operation	18

3.4  IO Input Query Command	19

3.5  Reboot reader	19

3.6  Config reading indicate	19

3.7  Query reading indicate	20

3.8  Config reading indicate pluse width of output IO	20

3.9  Query reading indicate pluse width of output IO	20

4.	ISO18000-6B Tag Operations	21

4.1  Tag Selection Parameter Configuration	21

4.2  Read Tag UID Code	21

4.3  Receiving Tag UID Code	22

4.4  Read Tag Data	22

4.5  Write Tag Data	23

4.6  Lock Tag Data Area	23

4.7  Query Tag Data Area Lock Status	23

5.	ISO18000-6C Tag Operation	24

5.1  Tag Selection Parameters Configuration	24

5.2  Read Tag EPC Code	24

5.3  Receiving EPC Code	25

5.4  Reading Tag TID Code Command	25

5.5  Receive tag TID code order	26

5.6  Write EPC code	26

5.7  Read user data Bank	26

5.8  Write user data Bank	27

5.9  Block write Bank data	27

5.10  Block erase Bank Data	28

5.11  Configure Visiting password	28

5.12  Change destruction password	28

5.13  Tag lock status setting	29

5.14  Tag Destruction	29

5.15  EAS Bit zone setting	30

5.16  Start EAS monitoring	30

6.	API Setting	30

6.1  API Versions information inquiry	30

6.2  Setting API trends library language type	31

6.3  Get Error Message	31

6.4  Get Error Code	31

Part VI	Appendix A: Error code list	32

# Overview

- API Function Package Introduction

The RFID devices provided by supplier would accompany with API function package. When user is developing RFID integrated application system, through calling this API function package, to control UHF series reader and read/write operation on RFID tags.

To call API function package, user doesn't have to know the underlying communication format between computer and reader, neither have to know the interface protocol or the process of reading/writing operation. The user only needs to focus on the functions, to simplify the difficulty of using RFID reader during the process of system integration.

- API Function Description

- Through API interface function, the following operations are available:

- Establish connection with reader based on serial, USB or Ethernet port.

- Configure and query reader system, RF and communication parameters.

- Achieve the basic operations on tag, such as read, write, lock, etc.

- Achieve the detection and control operations of reader IO input/output status.

# Call of API

- Environment Requirements

The following configurations are needed when user calls for API package:

Computer configuration: PIII 600MHz, 128M Memory, Windows XP/2003 Operation System, etc.

- File Included

API function package including the following files:

- RFIDAPI.dll

- RFIDAPI.lib

- RFIDAPIEXPORT.h

- API Call Methods

Add the files which Section 2.2 mentions to the project, and add the following sentence to source code: #include "RFIDAPIEXPORT.h", and then call the functions in it directly.

Please refer to the specific functions and features described in Part 4.

# Special Explanation

- About Tag

1.1 EPC Tag

EPC Class1 Gen2 is UHF frequency band RFID tag standard defined by EPC Global, which is currently known as EPC tag. The EPC tag is defined as ISO18000-6C standard after it is adapted by International Standardization Organization, the content of the two standards are basically the same. In this file and API function package, EPC tag is unified as ISO18000-6C or 6C tag, and will no longer be highlighted.

1.2 ISO8000-6B Tag

Currently, the ISO18000-6B tags are mostly from NXP, and general configuration is 224-byte data bank.

Figure.3-1 ISO18000-6B tag data bank configuration

The first 8bytes (address 0~7) is UID code, which is unique and locked in factory, only executing read operation.

8～223 bytes is general data bank, which can execute the operations such as write, read, lock and lock status querying.

When operating on ISO18000-6B general data bank, user must be aware that data address should not exceed the maximum bytes, which means parameter "start address" + "data length" not greater than 223.

Before operate on tag data bank, user should better confirm with tag provider for specific parameters.

1.3 ISO18000-6C Tag

There are several ISO18000-6C chip suppliers, and their data bank configurations are different due to applications and cost.

Popular configuration of data bank:

Figure.3-2 ISO18000-6B tag data bank configuration

TID Bank of ISO18000-6C tag is similar with UID Code of ISO18000-6B tag, and is required to be unique. While ISO18000-6C tag from some of these factories has no TID Bank, or with TID Bank but without unique TID code. There's only unified code from factory, some tags even has 4bytes TID Bank only.

EPC Code of ISO18000-6C tag is e-code, which is 0~64bytes according to protocol definition. Currently, tags from most factory is 12bytes (the actual length is greater than 12byte, but user usually doesn't involve in the rest content)

The length of USER Bank (user data area) is different due to different factory or model, some even without USER bank. Most tag factories use 28byte data bank.

RESERVED Bank including two areas: access password area and deactivating password area, 4byte each.

When operating on ISO18000-6C data banks, user must be aware that data address should not exceed the maximum bytes, which means parameter "start address" + "data length" not greater than 223.

Before operate on tag data bank, user should better confirm with tag provider for specific parameters.

- About Reader

2.1 Antenna Port

The fixed reader usually has several antenna ports (F805 with 4 antenna ports). Based on this, user can equip with multi-antenna to achieve one reader operates on multi-spots, or operates on the same spot from different angle to ensure tag identifying accuracy. The function of antenna port is the same, working with time rolling method. In tag operation process, user has to point out which one to use. When the "port number" value is "0x01～0x04", the corresponding reader antenna port is 1#~4#. If it's "0x00", this requires all the usable ports of reader to query in roll.

2.2 Multi Reader

- User application software can simultaneously control multiple readers simultaneously, for the reader's recognition through the following ways:

- Serial or USB connection is achieved through the serial port number. When initial the serial or USB port, initialization function would return an initialization handle, and every operation function provides a handle as a mark for identifying different readers.

- If using multi-bus mode like RS-485, the initialization handle is the same, but the data bus address frame difference.

- If using Ethernet connection, you have to initial an Ethernet with software for different IP address and returning to each handle, and then call a different handle to a different IP.

# API Function List

- API function package including five functions: Communication Control Function, System Parameter Configuration Function, Reader Operation Function, Tag Operation Function and API Configuration Function.

- Communication control function includes establishing intercommunication connection between computer and reader, and the relative functions in communication process control.

- System parameter configuration function is used to query the reader configuration parameters, including communication parameters, the RF parameters.

- Reader operation function is to control the reader implementing the manipulation applications as switching on/off carrier, IO operation.

- Tag operation function is the specific operation function as reading, writing, locking a tag. The following document will describe ISO18000-6B and ISO18000-6C separately.

- API configuration function is used to configuring relative information for querying API function package.

- Communication Control Function

| No. | Name of Function | Description |
| --- | --- | --- |
| 1 | UHF_TCPInit | This function is to initial configuration parameter of computer Ethernet. |
| 2 | UHF_COMInit | This function is to initial computer serial port and parameter. |
| 3 | UHF_USBInit | This function is to initial computer USB port and parameter. |
| 4 | UHF_Open | Create connection based on one of the serial port, USB port or Ethernet. |
| 5 | UHF_Close | Close the established connection. |
| 7 | UHF_Reconnect | Reconnect reader |
| 8 | UHF_HeartSend | Check the connection status of communication links |

- System Parameter Configuration Function

| No. | Name of Function | Description |
| --- | --- | --- |
| 1 | UHF_SysInfSet | To configure system parameter of reader. |
| 2 | UHF_SysInfQuery | To query system parameter of reader. |
| 3 | UHF_WorkModeSet | To set work mode of reader. |
| 4 | UHF_ParmOp | To operate the input/output of reader parameter list. |
| 5 | UHF_RFParaSet | To set reader RF parameter. |
| 6 | UHF_RFParaQuery | To query reader RF parameter. |
| 7 | UHF_CommunicatParaSet | To set reader communication parameter. |
| 8 | UHF_CommunicatParaQuery | To query reader communication parameter. |
| 9 | UHF_NetParaSet | To set reader network parameter. |
| 10 | UHF_NetParaQuery | To query reader network parameter. |
| 11 | UHF_TagOpParaSet | To set tag operation parameter |
| 12 | UHF_TagOpParaQuery | To query tag operation parameter |
| 13 | UHF_ExtendBroadParaSet | To set reader expansion board parameter. |
| 14 | UHF_ExtendBroadParaQuery | To query reader expansion board parameter. |
| 15 | UHF_TotalAntennaParmQuery | To query all RF ports parameters |
| 16 | UHF_AntennaParmQuery | To query Specified RF port Parameter |
| 17 | UHF_AntennaParmSet | To set RF port parameters |
| 18 | UHF_SetAntennaPortEnable | To set port enable |
| 19 | UHF_SetAntennaPower | To set port power |
| 20 | UHF_SetAntennaTime | To set port read time |

- Reader Operation Function

| No. | Function Name | Description |
| --- | --- | --- |
| 1 | UHF_PowerOff | To stop reading |
| 2 | UHF_CarrierWaveOp | To control the carrier operation of reader. |
| 3 | UHF_IOOperate | To control the IO output operation of reader. |
| 4 | UHF_IOStateQuery | To query the IO input status of reader. |
| 5 | UHF_Reboot | To reboot reader |
| 6 | UHF_Reading_IOConfig | To config buzzer status |
| 7 | UHF_Reading_IOQuery | To query buzzer status |
| 8 | UHF_IOPulseWidthSet | To config the pulse width of output IO |
| 9 | UHF_IOPulseWidthQuery | To query the pulse width of output IO |

- Tag Operation Function

| No. | Function Name | Description |
| --- | --- | --- |
| 1 | UHF_6BTagSelect | Command the reader to select 6B tag. |
| 2 | UHF_6BReadUIDCode | Command the reader to read UID code on 6B tag. |
| 3 | UHF_6BReadUserData | Command the reader to reader data on 6B tag data bank. |
| 4 | UHF_6BRevUIDMsg | To receive UID code of 6B tag, returning from reader. |
| 5 | UHF_6BWriteUserData | Command the reader to write data on 6B tag data bank. |
| 6 | UHF_6BTagLock | Command the reader to lock 6B tag data bank. |
| 7 | UHF_6CTagSelect | Command the reader to select 6C tag. |
| 8 | UHF_6CReadEPCCode | Command the reader to read EPC code on 6C tag. |
| 9 | UHF_6CRevEPCMsg | To receive the EPC code returning from reader. |
| 10 | UHF_6CReadTIDCode | Command the reader to read TID code of 6C tag |
| 11 | UHF_6CRevTIDMsg | To receive TID code of 6C tag returning from reader. |
| 12 | UHF_6CWriteEPCCode | Command the reader to rewrite EPC code of 6c tag. |
| 13 | UHF_6CReadUserData | Command the reader to read user data bank of 6C tag. |
| 14 | UHF_6CWriteUserData | Command the reader to write data to 6C tag user data bank. |
| 15 | UHF_6CWriteBankData | Command the reader to operate 6C tag Bank. |
| 16 | UHF_6CClearBankData | Command the reader to block-erase 6C tag Bank. |
| 17 | UHF_6CAccessPWDSet | Command the reader to rewrite access password of 6C tag. |
| 18 | UHF_6CDestroyPWDSet | Command the reader to rewrite destruction password of 6C tag. |
| 19 | UHF_6CTagLock | Command the reader to lock 6C tag. |
| 20 | UHF_6CTagKill | Command the reader to deactivate 6C tag. |
| 21 | UHF_6CEASFlagSet | Command the reader to set EAS bits of 6C tag. |
| 22 | UHF_6CEASMonitorEnable | Command the reader to monitor EAS. |

- API Configuration Function

| No. | Function Name | Description |
| --- | --- | --- |
| 1 | UHF_Copyright | Information querying function of API software. |
| 2 | UHF_SetLanguageType | Set function of API language type. |
| 3 | UHF_GetErrorMessage | Get err information |
| 4 | UHF_GetErrorCode | Get err code |

# API Function Description

- Communication Control Function

1.1  TCP Parameter Initialization

| Description | By an argument, this function is used to configure the computer's Ethernet applications, initialization of a SOCKET, to prepare a connection based on the Ethernet interface. |
| --- | --- |
| Prototype | bool UHF_TCPInit (void** pHandle,char *pHostName, int nsocketPort) |
| Parameter | pHandle | the preservation of opening ports handle |
|  | pHostName | reader IP address |
|  | nsocketPort | reader SOCKET port, default is 7086 |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

1.2  COM Port Parameter Initialization

| Description | By an argument, this function is to initial the specified computer COM port, preparing for the connection based on serial port. |
| --- | --- |
| Prototype | Bool UHF_COMInit(void** pHandle, unsigned char nBusAddr, char *pComNum, int nBaud) |
| Parameter | pHandle | the preservation of opening ports handle |
|  | nBusAddr | the Bus address, default is 0 |
|  | pComNum | COM1－COM4 communication mode is only valid in the COM |
|  | nBaud | serial communication speed, default is 19200 |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

1.3  USB Parameter Initialization

| Description | Reader USB interface, the current application is a virtual serial port, so the use of USB interface also need to initialize the COM port. Through the argument this function initializes the computer COM port, to prepare USB-based connection. |
| --- | --- |
| Prototype | Bool UHF_USBInit(void** pHandle,unsigned char nBusAddr,char * pUSBNum,int nBaud ) |
| Parameter | pHandle | the preservation of opening ports handle |
|  | nBusAddr | the Bus address, default is 0 |
|  | pUSBNum | COM1－COM4 (COM1-COM4 is virtual serial port, USB switching communication protocol) is only valid to USB communication mode. |
|  | nBaud | USB port communication speed, default is 152000 |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

1.4  UDP Parameter Initialization

| Description | By an argument, this function is used to configure the computer's Ethernet applications, initialization of a SOCKET, to prepare a connection based on the Ethernet interface. |
| --- | --- |
| Prototype | bool UHF_UDPInit (void** pHandle,char *pHostName, int nsocketPort) |
| Parameter | pHandle | the preservation of opening ports handle |
|  | pHostName | reader IP address |
|  | nsocketPort | reader udp port, default is 7088 |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

1.5  Establish Connection

| Description | Create connection based on one of the following interfaces, as serial port, USB port, Ethernet port or any other ports. |
| --- | --- |
| Prototype | bool UHF_Open(void* pHandle) |
| Parameter | pHandle | the preservation of opening ports handle |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

1.6  Close the Connection

| Description | Close the connection has been established. |
| --- | --- |
| Prototype | bool UHF_Close(void *pHandle) |
| Parameter | pHandle | the preservation of opening ports handle |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

1.7  Re-connect reader

| Description | Reconnect reader |
| --- | --- |
| Prototype | bool UHF_Reconnect(void *pHandle) |
| Parameter | pHandle | the preservation of opening ports handle |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

1.8  Check the connection

| Description | Check the connection status of communication links |
| --- | --- |
| Prototype | bool UHF_HeartSend (void *pHandle) |
| Parameter | pHandle | the preservation of opening ports handle |
| Return | true | Operation Success; |
|  | False | Operation Failed. |

- Configuration of System Information

2.1  System Information Setting

| Description | The function is used to set reader system configuration parameters, such as the name of readers, the passwords. |
| --- | --- |
| Prototype | bool UHF_SysInfSet (void * pHandle, unsigned char nType, unsigned char* pParm, unsigned char nLen) |
| Parameter | pHandle | the preservation of opening ports handle |
|  |  | configuration type of system information |
|  |  | nType | Definition | Length |
|  |  | 0 | Name of Reader | 8bytes |
|  |  | 10 | Access Password of Reader System | 6bytes |
|  | pParm | system parameter |
|  | nLen | length of system parameter |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

2.2  Query of System Information

| Description | This function is used to query the reader system information and other parameters, see the following query type as the "information type" defined. |
| --- | --- |
| Prototype | bool UHF_SysInfQuery (void* pHandle ,unsigned char nType, unsigned char *pPara, unsigned char *pLen) |
| Parameter | pHandle | the preservation of opening ports handle |
|  | nType | the information type for query(as following) |
|  | pParm | point to the pointer of memory which receives reader parameter data |
|  | nLen | pLen the length of pointed memory |
| Return | true | Operation Success; |
|  | false | Operation Failed. |
| Explanation: nType(information type) definition description: |
| nType | Definition | Length |
| 0x00 | Name of Reader | 8bytes |
| 0x01 | Model of Reader | 6bytes |
| 0x02 | Factory Serial No. of Reader | 8bytes |
| 0x03 | Software Version of Reader Processor | 4bytes |
| 0x04 | Software Version of Reader Decoding Unit | 4bytes |
| 0x05 | Hardware Version No. of Baseband Circuit | 4bytes |
| 0x06 | Hardware Version No. Of RF Circuit | 4bytes |

2.3  Configuration of Working Mode

| Description | This function is used to configure the working mode of the reader. |
| --- | --- |
| Prototype | bool UHF_WorkModeSet (void* pHandle ,unsigned nType) |
| Parameter | pHandle | the opening port handle |
|  | nType | the working mode to configure |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation:

nType(information type) definition description:

| Working Mode | Definition | Description |
| --- | --- | --- |
| 0x00 | Master-slave mode | Under the command of host computer, reader executes reading tag operation; |
| 0x01 | Preset Mode | The Reader executes tag operation based on preset command; |
| 0x02 | Trigger Mode | The reader triggers tag operation command according to IO input; |
| 0x03 | Timing Mode | According to the system clock timing, reader executes tag operation. |

2.4  Operation on System Parameter List

| Description | This function is used to operate parameter list of reader (for querying or configuring large quantity of reader parameter), including input/output whole or some part of the system parameter list. |
| --- | --- |
| Prototype | bool UHF_ParmOp (void* pHandle ,unsigned char nType, unsigned char nStartAddrr, unsigned char nLen, unsigned char *pData, unsigned char *pDataLen) |
| Parameter | pHandle | the opening port handle |
|  | nType | working mode of operating parameter list(as explanation) |
|  | nStartAddrr | to specify the start-address of operating reader parameter list |
|  | nLen | to specify the length of reader system parameter list |
|  | pData | incoming data, or outgoing data |
|  | pDataLen | length of pData |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation:

nType parameter list working mode:

| 0x00 | restore the system parameter list to factory settings |
| --- | --- |
| 0x01 | afferent system parameter list |
| 0x02 | efferent system parameter list |

Note: when working mode is 0x00, both start-address and operation lengths are meaningless.

2.5  Configuration of Carrier

| Description | This function is used for configuring parameter of reader RF carrier. |
| --- | --- |
| Prototype | bool UHF_RFParaSet (void* pHandle ,unsigned char nType, int nParaLen,unsigned char* pPara) |
| Parameter | pHandle | the opening port handle |
|  | nType | parameter type of the set parameter list(as explanation) |
|  | nParaLen | length of pPara |
|  | pPara | the set frequency table(as explanation) |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation:

"Parameter Type" defined as following, is a carrier parameter type ready to configure:

0x00   Frequency Hopping Table

"Frequency table"  is the values of frequency hopping table reader using, a combination of frequency points 0~15(CE and CN standard); a combination of frequency points 0~49(FCC standard).

2.6  Query Carrier Parameter

| Description | This function is used for querying parameter settings of reader carrier. |
| --- | --- |
| Prototype | Bool UHF_RFParaQuery (void* pHandle , unsigned char nType, unsigned char* pPara, unsigned char *pLen) |
| Parameter | pHandle | the opening port handle |
|  | nType | query the type of carrier parameter, definition as 5.2.5 |
|  | pPara | returning parameter of frequency table |
|  | pLen | incoming: length of pPara; Outgoing: length of frequency table |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

2.7  Configuration of Communication Parameter

| Description | This function is used to Bus communication parameters such as serial ports. |
| --- | --- |
| Prototype | bool UHF_CommunicatParaSet (void* pHandle ,unsigned char nType, unsigned char* pPara, unsigned char nLen) |
| Parameter | pHandle | the opening port handle |
|  | nType | configuration parameter type(as explanation) |
|  | pPara | reader serial Bus parameter |
|  | nLen | length of pPara |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation:

nType configuration parameter type:

| 0x00 | serial Bus device address |
| --- | --- |
| 0x01 | RS-232 Bus speed |
| 0x02 | RS-485 Bus speed |

Definition of serial Bus device address: when a reader is using multi-node Bus (such as RS-485 Bus), the reader node number is device address. The length of address is 1bytes, value 1~254, 0x00 and 0xff is broadcast address.

RS-232 Bus speed: communication speed of reader RS-232 serial Bus, and data defined as following

| 0x00 | 4800bps |
| --- | --- |
| 0x01 | 9600 bps |
| 0x02 | 19200 bps |
| 0x03 | 38400 bps |
| 0x04 | 57600 bps |
| 0x05 | 115200 bps |

RS-485 Bus speed: communication speed of RS-485 serial Bus, definition the same as RS-232 serial Bus

2.8  Query Communication Parameter

| Description | This function is used for querying communication parameter of reader serial Bus. |
| --- | --- |
| Prototype | bool UHF_CommunicatParaQuery (void* pHandle ,int nType, unsigned char* pPara,unsigned char *pLen) |
| Parameter | pHandle | the opening port handle |
|  | nType | configuration parameter type(as explanation) |
|  | pPara | query reader bus parameter |
|  | pLen | incoming: length of pPara; outgoing: length of reader bus parameter |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation: definition of nType is the same as 5.2.7.

2.9  Configuration of Network Parameter

| Description | This function is used to configure Ethernet parameter, such as reader IP address. |
| --- | --- |
| Prototype | bool UHF_NetParaSet (void* pHandle ,unsigned char nType, unsigned char* pPara, unsigned char nLen) |
| Parameter | pHandle | the opening port handle |
|  | nType | configuration parameter type(as explanation) |
|  | pPara | configuration Ethernet parameter data(as explanation) |
|  | nLen | length of pPara |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation:

nType is the parameter type:

| 0x01 | MAC address |
| --- | --- |
| 0x02 | IP address |
| 0x03 | TCP SOCKET number |
| 0x04 | UDP SOCKET number |

*IP configuration Ethernet IP parameters, totally 12bytes in turn including 4bytes IP address, 4bytes mask, 4bytes default gateway. It's not compatible with IPV6 format currently.

*SOCKET number when host computer and reader communicate via Ethernet, using the socket. This function is used for the reader to identify application program of host computer, the default socket number is 7086、7088. When the socket port is blocked by firewall or occupied by other applications in an Ethernet network system, user is available or legal to use this function to modify port number. Recommended to use with caution!

2.10  Query Network Parameter

| Description | This function is used to query Ethernet parameter, such as reader IP address. |
| --- | --- |
| Prototype | bool UHF_NetParaQuery(void* pHandle ,int nType, unsigned char* pPara,unsigned char *pLen) |
| Parameter | pHandle | the opening port handle |
|  | nType | query parameter type(as explanation) |
|  | pPara | the returning network parameter data |
|  | pLen | incoming: length of pPara; outgoing: actual returning length |
| Return | true | Operation Success; |
|  | false | Operation Failed. |
| Explanation: nType is parameter type, definition as 5.2.9 |
| 0x01 | MAC address |
| 0x02 | IP address |
| 0x03 | TCP SOCKET port number |
| 0X04 | UDP SOCKET port number |

2.11  Configuration of Tag Operation Parameter

| Description | This function is used to configure the parameters when a reader is operating to read/write tags. |
| --- | --- |
| Prototype | bool UHF_TagOpParaSet (void* pHandle ,unsigned char nType, unsigned char *pPara,unsigned char nLen) |
| Parameter | pHandle | the opening port handle |
|  | nType | configuration parameter type(as explanation) |
|  | pPara | configuration tag operation parameter |
|  | nLen | incoming: length of pPara; outgoing: parameter length of tag operation |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation:

nType is configuration parameter type, including:

| Type | Explanation | Returning information length |
| --- | --- | --- |
| 0x10 | Q value of the default | 1bytes |
| 0x11 | select parameter(BANK/address/mask/data) | Nbytes |
| 0x13 | default length of EPC code(the following is parameter configuration of IS018000-6B tag) | 1bytes |
| 0x21 | select parameter(type/address/mask/data) | Nbytes |

2.12  Query Tag Operation Parameter

| Description | This function is used to query the operation parameters when reader is operating on tags. |
| --- | --- |
| Prototype | bool UHF_TagOpParaQuery (void* pHandle ,unsigned char nType, unsigned char* pPara, unsigned char *pLen) |
| Parameter | pHandle | the opening port handle |
|  | nType | configuration parameter type(as explanation) |
|  | pPara | pointing to the memory pointer which saving configuration parameters |
|  | Len | incoming: length of pPara; outgoing: parameter length of tag operation |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation:

nType is parameter type, definition as part V 2.11

2.13  Configuration of Expansion Board Parameter

| Description | This function is used to configure expansion board parameters. |
| --- | --- |
| Prototype | bool UHF_ExtendBroadParaSet (void* pHandle ,unsigned char nType, unsigned char pSendChunnel) |
| Parameter | pHandle | the opening port handle |
|  | nType | configuration tag operation parameter type |
|  |  | 0 IO output operation 1 IO input operation |
|  | pSendChunnel | configuration tag operation parameter |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

2.14  Query Expansion Board Parameter

| Description | This function is used to query expansion board parameters. |
| --- | --- |
| Prototype | bool UHF_ExtendBroadParaQuery (void* pHandle ,unsigned char nType, char* pPara, unsigned char* pLen) |
| Parameter | pHandle | the opening port handle |
|  | nType | configuration tag operation parameter type |
|  |  | 0 IO output operation 1 IO input operation |
|  | pPara | query parameters |
|  | pLen | incoming: length of pPara; outgoing: length of query parameters |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

2.15  Query RF Port Parameter

| Description | This function is used to query RF port parameter of reader. |
| --- | --- |
| Prototype | Bool UHF_TotalAntennaParmQuery(void* pHandle,unsigned char *szAntennaPara,unsigned char *pLen) |
| Parameter | pHandle | the opening port handle |
|  | szAntennaPara | all RF port parameters(as explanation) |
|  | pLen | incoming: length of szAntennaPara; outgoing: all RF port parameters length |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation:

all RF port parameters including

| Port Enable | 4bytes | Antenna port enable |
| --- | --- | --- |
| Power Output | 4bytes | Antenna port output power |
| Cycling Query | 4bytes | Antenna port cycling query |

"Port Enable" configuration parameter length is 4bytes, in turn for antenna 1~4 port configuration, 0x00 is "forbid", 0x01 is "allow".

"Power Output" configuration parameter length is 4bytes, in turn for antenna 1~4 port power output parameter (0x00~0x0A), and data defined as following

| 0x00 | 20.0(dBm) |
| --- | --- |
| 0x01 | 21.0(dBm) |
| 0x02 | 22.0(dBm) |
| 0x03 | 23.0(dBm) |
| 0x04 | 24.0(dBm) |
| 0x05 | 25.0(dBm) |
| 0x06 | 26.0(dBm) |
| 0x07 | 27.0(dBm) |
| 0x08 | 28.0(dBm) |
| 0x09 | 29.0(dBm) |
| 0x0A | 30.0(dBm) |

"Cycling Query" configuration parameter length is 4bytes, in turn for antenna 1~4 port cycling query parameter, which is the working time for the specific port, working time=time parameter*100ms.

2.16  Query Specified RF port Parameter

| Description | This function is used to query RF parameter of reader parameter table. |
| --- | --- |
| Prototype | bool UHF_AntennaParmQuery (void* pHandle, unsigned char nAntenna, unsigned char * pAntennaEnable, unsigned char *pAntennaPower, unsigned char *pAntennaQueryTime ) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | the antenna port number to configure |
|  | nAntennaEnable | antenna port enable, 0x00 is "forbid", 0x01 is "allow" |
|  | nAntennaPower | power output, in unit of dBm |
|  | nAntennaQueryTime | in cycling query mode, the working time of this port(ms) |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

2.17  Configuration of RF port parameter

| Description | This function is used to configure RF port parameter of reader parameter table. Prototype: |
| --- | --- |
| Prototype | bool UHF_AntennaParmSet(void* pHandle ,unsigned char *pPara,unsigned char nLen ) |
| Parameter | pHandle | the opening port handle |
|  | pPara | configure RF port parameter of reader parameter table(as explanation) |
|  | nLen | parameter length, usually is 12bytes |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation:

all RF port parameters including

| Port Enable | 4bytes | Antenna port enable |
| --- | --- | --- |
| Power Output | 4bytes | Antenna port output power |
| Cycling Query | 4bytes | Antenna port cycling query |

"Port Enable" configuration parameter length is 4bytes, in turn for antenna 1~4 port configuration, 0x00 is "forbid", 0x01 is "allow".

"Power Output" configuration parameter length is 4bytes, in turn for antenna 1~4 port power output parameter (0x00~0x0A), and data defined as following

| 0x00 | 20.0(dBm) |
| --- | --- |
| 0x01 | 21.0(dBm) |
| 0x02 | 22.0(dBm) |
| 0x03 | 23.0(dBm) |
| 0x04 | 24.0(dBm) |
| 0x05 | 25.0(dBm) |
| 0x06 | 26.0(dBm) |
| 0x07 | 27.0(dBm) |
| 0x08 | 28.0(dBm) |
| 0x09 | 29.0(dBm) |
| 0x0A | 30.0(dBm) |

"Cycling Query" configuration parameter length is 4bytes, in turn for antenna 1~4 port cycling query parameter, which is the working time for the specific port, working time=time parameter*20ms.

2.18  Specified RF port Enable Configuration

| Description | This function is used to configure reader specified RF port enable. |
| --- | --- |
| Prototype | bool UHF_SetAntennaPortEnable (void* pHandle, unsigned char nAntenna, unsigned char nEnable ) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | the antenna port number for configuring |
|  | nEnable | enable configuration |
|  |  | 0x00 forbid 0x01 allow |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

2.19  Specified RF port Power Configuration

| Description | This function is used to configure reader specified RF port power. |
| --- | --- |
| Prototype | bool UHF_SetAntennaPower (void* pHandle,unsigned char nAntenna,unsigned char nPower ) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | RF port number 1~4 |
|  | nPower | Configuration power(0x00~0x0A) |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation:

nPower defined as following

| 0x00 | 20.0(dBm) |
| --- | --- |
| 0x01 | 21.0(dBm) |
| 0x02 | 22.0(dBm) |
| 0x03 | 23.0(dBm) |
| 0x04 | 24.0(dBm) |
| 0x05 | 25.0(dBm) |
| 0x06 | 26.0(dBm) |
| 0x07 | 27.0(dBm) |
| 0x08 | 28.0(dBm) |
| 0x09 | 29.0(dBm) |
| 0x0A | 30.0(dBm) |

2.20  Specified RF port Cycling Query Configuration.

| Description | This function is used to configure each RF port polling time, according to the importance of each port and reading requirements to set time, thus to optimize system. |
| --- | --- |
| Prototype | bool UHF_SetAntennaTime (void* pHandle,unsigned char nAntenna,unsigned char nTime ) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | RF port number 1~4 |
|  | nTime | set polling time, working time=polling time*100ms |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

- Reader Operation Functions

3.1  Stop Reading

| Description | This function is used to inform the reader stop the current executing instructions related to operation on tags. |
| --- | --- |
| Prototype | bool UHF_PowerOff(void *pHandle); |
| Parameter | pHandle | the opening port handle |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

3.2  Carrier Operation

| Description | This function is used to control reader carrier, opening the carrier and output or stop outputting by specified RF port. Knowing from principle of radio frequency identification, when reading tags the reader is required to have continuous carrier output, and providing energy for tag operation. This function is used to control open/stop of carrier. But in actual application, reader would auto-open carrier in executing tag operation and would auto-stop after tag operation finished. Thus users usually don't need to use it. |
| --- | --- |
| Prototype | bool UHF_CarrierWaveOp(void* pHandle ,unsigned char nType, unsigned char nPort) |
| Parameter | pHandle | the opening port handle |
|  | nType | carrier operation mode |
|  |  | 0x00 open 0x01 stop |
|  | nPort | the open carrier port 1~4 |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

3.3  IO Output Operation

| Description | This function is used to control reader operation on multi IO output port. |
| --- | --- |
| Prototype | bool UHF_IOOperate(void* pHandle,unsigned char nPort,unsigned char nState) |
| Parameter | pHandle | the opening port handle |
|  | nPort | IO output port number 1~4 |
|  |  | 0x00 all ports 0x01 port 1 0x02 port 2 0x03 port 3 0x04 port 4 |
|  | nState | IO output power level state(as explanation) |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation:

nState output state:

| 0x00 | specify IO switch to low power level state |
| --- | --- |
| 0x01 | specify IO switch to high power level state |
| 0x02 | specify IO output 10ms positive pulse signal |
| 0x03 | specify IO output 10ms negative pulse signal |

3.4  IO Input Query Command

| Description | This function is used to query reader IO input port status. |
| --- | --- |
| Prototype | bool UHF_IOStateQuery(void* pHandle,unsigned char *pState) |
| Parameter | pHandle | the opening port handle |
|  | pState | power level state pointer of input port |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation:

port status is indicated with bytes:

| 0x00 | specify IO switch to low power level state |
| --- | --- |
| 0x01 | specify IO switch to high power level state |
| 0x02 | specify IO output 10ms positive pulse signal |
| 0x03 | specify IO output 10ms negative pulse signal |
| Bit | Bit7 | Bit 6 | Bit 5 | Bit 4 | Bit 3 | Bit 2 | Bit 1 | Bit 0 |
| Definition | Reserve | Reserve | Reserve | Reserve | Reserve | Reserve | Port 2 | Port 1 |

Port Status: 0 low power level; 1 high power level

3.5  Reboot reader

| Description | This function is used to reboot reader |
| --- | --- |
| Prototype | bool UHF_Reboot(void* pHandle,unsigned char nMode) |
| Parameter | pHandle | the opening port handle |
|  | nMode | 0x00 general 0x01 reboot |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

3.6  Config reading indicate

| Description | Config reading indicate |
| --- | --- |
| Prototype | bool UHF_Reading_IOConfig (void* pHandle,unsigned char nConfigBit) |
| Parameter | pHandle | the opening port handle |
|  | nConfigBit | Bit7 Bit6 Bit5 Bit4 Bit3 Bit2 Bit1 Bit0 R R R IO4 IO3 IO2 IO1 buzzer 0 disable 1 enable (R: Reserve) |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

3.7  Query reading indicate

| Description | Query reading indicate |
| --- | --- |
| Prototype | bool UHF_Reading_IOQuery (void* pHandle,unsigned char* pConfigBit) |
| Parameter | pHandle | the opening port handle |
|  | nConfigBit | Bit7 Bit6 Bit5 Bit4 Bit3 Bit2 Bit1 Bit0 R R R IO4 IO3 IO2 IO1 buzzer 0 disable 1 enable (R: Reserve) |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

3.8  Config reading indicate pluse width of output IO

| Description | Config reading indicate pluse width of output IO |
| --- | --- |
| Prototype | bool UHF_IOPulseWidthSet (void* pHandle,unsigned char nIOPort, unsigned char nWidth) |
| Parameter | pHandle | the opening port handle |
|  | nIOPort | Config IO port(0-4):port 0 is buzzer, port 1\port 2\port3\port4 is IO port |
|  | nWidth | Pulse width (unit100ms) |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

3.9  Query reading indicate pluse width of output IO

| Description | Query reading indicate pluse width of output IO |
| --- | --- |
| Prototype | bool UHF_IOPulseWidthQuery (void* pHandle,unsigned char nIOPort, unsigned char* pWidth) |
| Parameter | pHandle | the opening port handle |
|  | nIOPort | Config IO port(0-4):port 0 is buzzer, port 1\port 2\port3\port4 is IO port |
|  | nWidth | Pulse width (unit100ms) |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

- ISO18000-6B Tag Operations

4.1  Tag Selection Parameter Configuration

| Description | This function is used to configure selective parameters when reader operates on ISO18000-6B tags. Reader would use the selected parameter to operate on ISO18000-6B tag next time, and realizing selective operation on multi ISO18000-6B tags of some type or one tag(UID code or several bytes in data, equal, not equal, greater than/ less than the set data). |
| --- | --- |
| Prototype | bool UHF_6BTagSelect ( void* pHandle, unsigned char nType, unsigned char nStartAddr, unsigned char nDataBite, unsigned char * Data ) |
| Parameter | pHandle | the opening port handle |
|  | nType | match type(as explanation) |
|  | nStartAddr | start address of match data |
|  | nDataBite | match mask |
|  | Data | 8bytes for matching data |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation:

definition of match type

| 0x00 | SELECT | Equal |
| --- | --- | --- |
| 0x01 | SELECT | Not equal |
| 0x02 | SELECT | Greater than |
| 0x03 | SELECT | Less than |
| 0x04 | UNSELECT | Equal |
| 0x05 | UNSELECT | Not equal |
| 0x06 | UNSELECT | Greater than |
| 0x07 | UNSELECT | Less than |

Match the data start address: Indicating the start address to match the data, the maximum of match data should not exceed tag data bank. Currently, general data bank of ISO18000-6B tag is 224bytes, so the maximum is 216bytes.

Before using this function, user should better ask tag provider fot the length of tag data bank.

Match the data mask bit: Indicating from start address, which bytes are matching with matched data.

Match Data: Give the data which is to match tag data bank data, totally 8bytes.

Select command used to configure the reader back to the operating instructions specified only for a class of or one tag; the reader would cache the received parameter after receiving the selection instruction. On executing the next ISO18000-6B tag operation command, adding the parameter to the SELECT command (before sending tag operation command, every reader will send SELECT command), and enabling the command valid only to match tag.

If the reader doesn't receive tag selection command before executing tag operation command, the sending of command would use the default selected parameter.

Once the selection parameter configuration command is successful, the reader's next operation on ISO18000-6B tag will follow the configured parameter. After the operation, the selection parameter would restore to default, which means this command is a one-time operation, only effective for next reading.

If you need to use some selection parameter for long-term, you can execute "Tag Operation Parameter Configuration" command to modify the default tag selection command.

Selection command doesn't provide query function, when host computer is not sure about current parameters, and sending this command for re-configuration.

4.2  Read Tag UID Code

| Description | This function is used to send "read ISO18000-6B tag UID code" command to reader. |
| --- | --- |
| Prototype | bool UHF_6BReadUIDCode (void *pHandle,unsigned char nAntenna,unsigned char nType) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | operating antenna number(0-cycling query antenna, 1---antenna port 1, 2--antenna port 2, 3---antenna port 3, 4---antenna port 4) |
|  | nType | operation mode |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation:

nType operation mode

| 0x00 | Single reading mode, the reader would read only once and send all the tags' UID code been read, returning to host computer in turn, and later reader would auto-stop reading. |
| --- | --- |
| 0x01 | Cycling reading mode, reader returns all the UID code collected to host computer, and will auto-carry on this reading operation, till the host computer issue "stop operation" and then the reading operation will halt. |

4.3  Receiving Tag UID Code

| Description | This function starts receiving operation to receive tag UID code returning from reader. |
| --- | --- |
| Prototype | int UHF_6BRevUIDMsg (void *pHandle, unsigned char* nAntenna, unsigned char* pUIDData, unsigned char* nUIDLen) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | antenna number which reads UID code |
|  | pUIDData | the received UID code data |
|  | nUIDLen | incoming: length of pUIDData; outgoing: length of UID data(8bytes) |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

4.4  Read Tag Data

| Description | This function is used to reader data in tag data bank. |
| --- | --- |
| Prototype | bool UHF_6BReadUserData ( void *pHandle ,unsigned char nAntenna,unsigned char nType,unsigned char * pTagID, unsigned char nStartAddr,unsigned char nReadLen, unsigned char *pdata, unsigned char dataLen) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | antenna number in read operation |
|  | nType | operating mode, set as 0 |
|  | pTagID | the target tag 8bytesUID code to read |
|  | nStartAddr | first target address of data bank to read |
|  | nReadLen | the target data length |
|  | pdata | the buffer pointer which stores the collected data |
|  | dataLen | length of pdata |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation:

- This command requires reader to read within specified tag data bank some specified data content and returns to host computer.

- This is a single tag operation command, and must fill in specified tag UID code in "tag UID" parameter.

- Read tag "data start address", which range is from 0x00 to the last bytes address of data area, "data length" range is from 1 to tag total length of data area. It is required to meet "data area start address" + "data area length" not exceeding tag maximum address.

*ISO18000-6B protocol defines reader in executing data area reading operation, the maximum is 8bytes each time, and to read more bytes, multiple operations is needed. This API can automatically check and cut off long data, so users don't need to write many times. It is recommended to write 64bytes every time, as prolonged operation increases the probability of interference.

* The general ISO18000-6B tag data bank is 224bytes, and the field maximum value is 22. Before using this function, user should better query tag provider for its data bank length parameter.

4.5  Write Tag Data

| Description | This function is used to write data into tag data bank. |
| --- | --- |
| Prototype | bool UHF_6BWriteUserData (void* pHandle, unsigned char nAntenna, unsigned char nType, unsigned char *pTagID, unsigned char nStartAddrr, unsigned char *pValue, unsigned char *nLen) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | antenna number in write operation |
|  | nType | operating mode, set as 0 |
|  | pTagID | the target tag 8bytesUID code to write |
|  | nStartAddr | the first address to write in data bank(greater than 0x08) |
|  | pValue | the target data to write |
|  | nLen | incoming: length of pValue; outgoing: actual wrote data length |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

*ISO18000-6B protocol defines first 8bytes of tag as UID, usually has been locked in the factory, non-writable.

*ISO18000-6B protocol defines when a reader executing data bank writes operation only 4bytes writable each time. If you want to write more bytes, the reader needs to execute several times of writing operation. But users don't need to read/write more times, as this API can automatically check and cut off long data, so users don't need to write many times. It is recommended to write 64bytes every time, as prolonged operation increases the probability of interference.

4.6  Lock Tag Data Area

| Description | This function is used to execute tag data in non-reversible lock operation. The locked data bank data can not be rewritten or unlocked. |
| --- | --- |
| Prototype | bool UHF_6BTagLock (void* pHandle, unsigned char nAntenna, unsigned char nType, unsigned char *pTagID, unsigned char nStartAddrr, unsigned char nLen) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | antenna number which executing lock operation |
|  | nType | lock operation mode, 0x00 is locked status |
|  | pTagID | 8bytes UID code which is to write in tag |
|  | nStartAddrr | first address of data bank to be locked, 8~224bytes |
|  | nLen | Data length of data bank to be locked, "length + start address" should not exceed tag's maximum length. |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation:

This command controls reader to execute lock operation on data bank.

Currently, general data bank of ISO18000-6B tags is 224bytes, and the maximum field is 224. Before using this function, users are recommended to ask the provider for length of tag data bank.

4.7  Query Tag Data Area Lock Status

| Description | This function is used to query tag data bank lock status. |
| --- | --- |
| Prototype | bool UHF_6BTagLockQuery (void* pHandle, unsigned char nAntenna, unsigned char * pTagID, unsigned char nStartAddrr, unsigned char nLen, unsigned char *pData, unsigned char nDataLen) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | antenna number on querying operation |
|  | pTagID | 8bytes tag ID |
|  | nStartAddrr | first address of queried data bank, 8~224bytes |
|  | nLen | data length of queried data bank, "length + start address" should not exceed tag's maximum length |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

- ISO18000-6C Tag Operation

5.1  Tag Selection Parameters Configuration

| Description | This function is used to configure the selection parameters when reader operates on the ISO18000-6C Tag. The reader will use the selection parameter at the next operation. This realizes making selectivity operation on multi ISO18000-6C Tags with similar properties (EPC code, TID code or some bytes data in user data field). |
| --- | --- |
| Prototype | bool UHF_6CTagSelect (void *pHandle, unsigned char nBank ,unsigned char nStartAddr,unsigned char MaskBit, unsigned char *Data ,unsigned char Datalength,unsigned char nSessionZone, unsigned char nActiveFlag, unsigned char nCutFlag ) |
| Parameter | pHandle | the opening port handle |
|  | nBank | specify matching data field Bank(as explanation) |
|  | nStartAddr | the start address of the specified matching data field Bank |
|  | MaskBit | specify matching data bit number |
|  | Data | specify matching data |
|  | Datalength | data length |
|  | nSessionZone | specify matching data session field(as explanation) |
|  | nActiveFlag | specify matching data activity flag(as explanation) |
|  | nCutFlag: | specify matching data cut off flag(as explanation) |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation:

Bank matching data field: indicating the data field need match

| 0x01 | EPC data code |
| --- | --- |
| 0x02 | TID data code |
| 0x03 | USER data code |

The first address of the matching data: It indicates the start address of the matching data. Tags from different manufacturers have different data are size, so does the start address range, but the max-size could not exceed the maximum matching data bank of tag. For specific data, please check with the data user manual. If you are not sure of the maximum data bank, try to read tag operation Band before any other operation. And through this way confirms the maximum data bank of tag. This field uses EVB data format, length of data is changeable. Please see the appendix A for definition of EVB format.

Match the Number of Bit: Indicates the bits of data for matching, taking Bit as a unit. Be aware that start address of matched data + matching bit number should not exceed the maximum value of data bank.

Match Data: Indicates the data for matching, and matched data is counted by bits while command is transmitted in bytes. When the match data is not full bytes, reader program will automatically cut the extra bits according to match bit number.

This function is used to set the reader tag operating parameters.

Selection command is only valid to next one operation. If you want it to be valid to all command, you can use "tag operation configuration command" to set the match rule as default.

Example:

Match Bit number = 13, then the match data should be

| B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| D | D | D | D | D | D | D | D | D | D | D | D | D | 0 | 0 | 0 |

D: Bit Data   0: Additional Bits

5.2  Read Tag EPC Code

| Description | This function is used to instruct the reader executing "reader EPC code command". |
| --- | --- |
| Prototype | bool UHF_6CReadEPCCode (void *pHandle,unsigned char nAntenna, unsigned char nType, unsigned char nTagCount) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | the antenna number which is operating (0 is antenna rolling read, 1--antenna 1, … , 4--antenna 4) |
|  | nType | operating mode |
|  |  | 00: Reader returns EPC code of the same tag to host computer only once, and requires the host computer giving "return data confirmation" after receiving the EPC code. 01: Reader returns all the EPC code it collected to host computer, and doesn't require the host computer returning "return data confirmation". Till host computer sends "Amp off" command, the reader stops reading. This operating mode is commonly used. |
|  | nTagCount | This function will also estimate the tag number, estimating the maximum tag number read simultaneously under working environment. It is designed to read 250pcs simultaneously, while the actual read tags exceed 500pcs. |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

5.3  Receiving EPC Code

| Description | This function is used to receive the EPC code reader returns, probably multiple EPC code is returned. |
| --- | --- |
| Prototype | int UHF_6CRevEPCMsg (void *pHandle, unsigned char* nAntenna, unsigned char* pEPCData, unsigned char* nEPCLen) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | antenna number which reads EPC code |
|  | pEPCData | returning EPC code data |
|  | nEPCLen | incoming: length of pEPCData; outgoing: length of EPC data, usually is 12 |
| Return | 1 | Operation Success; |
|  | 0 | Operation Failed. |
|  | 2 | Heart beat package reader returns. |

5.4  Reading Tag TID Code Command

| Description | This function is used to instruct reader reading "tag TID code". |
| --- | --- |
| Prototype | bool UHF_6CReadTIDCode(void *pHandle, unsigned char nAntenna, unsigned char nType, unsigned char nTagCount) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | the antenna number which is operating (0 is antenna rolling read, 1--antenna 1, …, 4--antenna 4) |
|  | nType | operating mode |
|  |  | 00: Reader returns TID code of the same tag to host computer only once, and requires the host computer giving "return data confirmation" after receiving the EPC code. 01: Reader returns all the TID code it collected to host computer, and doesn't require the host computer returning "return data confirmation". Till host computer sends "Amp off" command, the reader stops reading. This operating mode is commonly used. |
|  | nTagCount | This function will also estimate the tag number, estimating the maximum tag number read simultaneously under working environment. It is designed to read 250pcs simultaneously, while the actual read tags exceed 500pcs. |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation:

EPC global sets default bit of TID Bank of EPC Class1 Gen2 tags as 4 double-bits (words), which is 64bits. As the TID is getting marginalization in EPC applications, some factories even cancelled TID Bank. Reader underlying protocol will support different length of TID code.

5.5  Receive tag TID code order

| Description | This function is used to receive the TID code sent by the ISO18000-6C Tag. |
| --- | --- |
| Prototype | int UHF_6CRevTIDMsg (void *pHandle, unsigned char* nAntenna, unsigned char* pTIDData, unsigned char* nTIDLen) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | the antenna port number when operating tags(1-4) |
|  | pTIDData | TID data return by the reader |
|  | nTIDLen | when input this is the pTIDData length and when output this is the length of TID data |
| Return | 1 | Operation Success; |
|  | 0 | Operation Failed. |
|  | 2 | The reader returns new TID. |

5.6  Write EPC code

| Description | This function is used to write EPC code |
| --- | --- |
| Prototype | bool UHF_6CWriteEPCCode(void* pHandle, unsigned char nAntenna, unsigned char nType, unsigned char *pAccessPWD, unsigned char *pWriteData, unsigned char nLen ) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | the antenna port number when operating tags(1-4) |
|  | nType | the operation type, the value is 0x00 |
|  | pAccessPWD | the password for visiting Tag, default value is 4 bytes 0 |
|  | pWriteData | the EPC code data needed to write in the Tag |
|  | nLen | the length of the pWriteData |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation:

This instruction is used to write EPC code in the Tag.

EPC code length: Length of EPC code for setting Tag and the basic unit is double bytes(words).According to the EPC protocol the value range is 0x00~32H(when setting 00 the EPC Tag will be initialized to empty Tag).EPC global division rule that the EPC code default length is 6 double bytes.

EPC protocol requires the EPC data must be written by words unit and must be written continuously. To simplify the write operation, the reader is designed to only accept read and write EPC data use the starting position as the first address. And it has nonsupport to modify one middle data in the EPC code

There has different EPC data field size in Tags come from different manufacturers. So if the "EPC data length" is more the maximum EPC data filed length the operation will be fail and return the corresponding error code.

Before write the Tag the antenna port must be explicit.

5.7  Read user data Bank

| Description | This function is used to get to User Bank data in ISO18000-6C Tag. |
| --- | --- |
| Prototype | bool UHF_6CReadUserData(void* pHandle, unsigned char nAntenna, unsigned int StartAddr, unsigned int nToReadLen, unsigned int nWaitTime ,unsigned char * UserData,unsigned char* pDataLen) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | the antenna port number when operating tags(1-4) |
|  | StartAddr | the start address for data reading |
|  | nLength | This is length of the reading data in the target tag, double-byte write and read. If length is 1 then read 2 bytes data or if length is 2 then read 4 bytes data and so on |
|  | nWaitTime | the overtime for data reading(Calculated by ms unit, for 1 s the value is 1000 ) |
|  | UserData | the data get from User Bank |
|  | pDataLen | when input this the length of the UserData and when output this is the length of the reading data field |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation:

This function is used to configure the relevant parameter about the reader Tag operations.

There has different User Bank size in Tags come from different manufacturers. So before read please check the data sheet to make sure the total length (User data Bank first address +User data length) is no more than the User data Bank length. Or the operation will be fail and return the corresponding error code.

Here is no user data Bank in some tag, so when execute the operation the Tag will return error code.

"Maximum Tag data field length" is 64,when read more than 64 bytes data the upper computer should take multi read operations(This is limited by the FPGA decode field size).

5.8  Write user data Bank

| Description | This function is used to write data in user data Bank of ISO18000-6C Tag. |
| --- | --- |
| Prototype | bool UHF_6CWriteUserData (void* pHandle, unsigned char nAntenna, unsigned char nType, unsigned char *pAccessPWD, unsigned int nStartAddr, unsigned int nWaitTime, unsigned char *pWriteData, unsigned int *pToWriteLen) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | the antenna port number when operating tags(1-4) |
|  | nType | the operation type, the value is 0 |
|  | pAccessPWD | the password for visiting Tag, default value is 4 bytes 0 |
|  | nStartAddr | the start address for data writing |
|  | inWaitTime | the overtime for data writing(Calculated by ms unit, for 1 s the value is 1000) |
|  | pWriteData | the data for writing in data Bank of the Tag |
|  | pToWriteLen | When input this is the length of the user data Bank and when output this is the length data actual writing in the data. Word (double byte) is the unit. |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation:

There has different User Bank size in Tags come from different manufacturers. So before write please check the data sheet to make sure the total length (User data Bank first address +User data length) is no more than the User data Bank length. Or the operation will be fail and return the corresponding error code.

There is no user data Bank in some tag, so when execute the operation the Tag will return error code.

The start address takes the EVB format. So the data length is variation. For the concrete EVB format please check in Appendix A.

"Write the tag data Bank" means the largest size can write in the data Bank. As the read operation, the reader at a time can write a word (double byte) data and the Tag need 20ms to write the data. When write too much data the probability for PF communication interfering between Tag and reader will increase. It is suggested that upper computer can maximum write 8 words at a time to the reader and divide data in several writing times when the data is larger than the limit.

Please ask supplier to get User data Bank length etc information.

5.9  Block write Bank data

| Description | This function is used to block write Bank data of ISO18000-6C Tag. |
| --- | --- |
| Prototype | bool UHF_6CWriteBankData (void* pHandle, unsigned char nAntenna, unsigned char nType, unsigned char *pAccessPWD, unsigned char nBank, unsigned char *pWriteData, unsigned char nLen) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | the antenna port number when operating tags(1-4) |
|  | nType | the operation type, default value is 0 |
|  | pAccessPWD | the password for visiting Tag, default value is 4 bytes 0 |
|  | nBank | Bank for Tag data writing |
|  | pWriteData | the user data for writing in the Tag |
|  | nLen | the length of the writing data |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

5.10  Block erase Bank Data

| Description | This function is used to block erase Bank data of ISO18000-6C Tag. |
| --- | --- |
| Prototype | bool UHF_6CClearBankData (void* pHandle, unsigned char nAntenna, unsigned char nType, unsigned char *pAccessPWD, unsigned char nBank, unsigned char nStartAddr, unsigned char nLen) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | the antenna port number when operating tags(1-4) |
|  | nType | the operation type, default value is 0 |
|  | pAccessPWD | the access password for visiting Tag, default value is0x00 |
|  | nBank | bank for Tag data writing |
|  | nStartAddr | the start address of the Tag data for erasing |
|  | nLen | the length of Tag data for erasing |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

5.11  Configure Visiting password

| Description | This function is used to set visiting password of ISO18000-6C tag. |
| --- | --- |
| Prototype | bool UHF_6CAccessPWDSet (void *pHandle, unsigned char nAntenna, unsigned char nType, unsigned char *pOrgPWD, unsigned char *pNewPWD) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | the antenna port number when operating tags(1-4) |
|  | nType | in this operation the value is 0 |
|  | pOrgPWD | the primary 4 bytes visiting password, the default value is 4 bytes 0 |
|  | pNewPWD | the new 4 bytes visiting password |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation:

The default visiting password is 4 bytes 0

If the Bank the password in is not locked, zero passwords can also execute the write operation (Get details in EPC protocol).

5.12  Change destruction password

| Description | This function is used to Change the destruction password of ISO18000-6C Tag. |
| --- | --- |
| Prototype | bool UHF_6CDestroyPWDSet (void *pHandle, unsigned char nAntenna, unsigned char *pAccessPWD, unsigned char nType, unsigned char *pDestroyPWD ) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | the antenna port number when operating tags(1-4) |
|  | pAccessPWD | password for Tag visiting,4Bits |
|  | nType | in this operation the value is 0 |
|  | pDestroyPWD | 4 Bytes password for Tag destruction |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation：

Visiting password: This password is for visiting the Tag. If the Tag destruction password is locked, the right visiting password is need to change the destruction password.

New destruction password: This password is a new one for destruction and the default value is "00000000".

EPC Protocol need nonzero password for the destruct operation.

If the Bank the password in is not locked, zero passwords can also execute the write operation (Get details in EPC protocol).

5.13  Tag lock status setting

| Description | This function is used to set the tag lock status. |
| --- | --- |
| Prototype | bool UHF_6CTagLock (void *pHandle, unsigned char nAntenna, unsigned char *pAccessPWD, unsigned char nType, unsigned char nBank) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | the antenna port number when operating tags(1-4) |
|  | pAccessPWD | password for tag visiting(4Bits) |
|  | nType | the lock type, see the definition in the explanation. |
|  | nBank | the executing Bank，see the definition in the explanation. |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation：

Bank type：ISO18000-6C Every Bank of the tag can have lock operation independently and be configured is different lock status. It need to point the target Bank in the lock operation.

| Code | definition |
| --- | --- |
| 0x00 | the whole Bank |
| 0x01 | TID Bank |
| 0x02 | EPC Bank |
| 0x03 | USER Bank |
| 0x04 | password for visiting |
| 0x05 | password for destruction |

Lock operation type：ISO18000-6C protocol defines the following 4 lock operation.

| Code | Definition |
| --- | --- |
| 0x00 | Lock |
| 0x01 | Deblocking |
| 0x02 | Permanent Lock |
| 0x03 | Permanent Open |

The TID field in the EPC tag has been written with TID code and is configured irreversible permanent status. So there is no effect on TID field when execute "Unlock all the Blank” operation.

5.14  Tag Destruction

| Description | This function is used to conduct Kill operation on tags |
| --- | --- |
| Prototype | bool UHF_6CKillTag (void *pHandle, unsigned char nAntenna,unsigned char *pDestroyPWD, unsigned char *pEPC, int nEPCLen) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | the antenna port number when operating tags(1-4) |
|  | pDestroyPWD | password for tag destruction(4Bits） |
|  | pEpc | EPC code for the target tag |
|  | nEPCLen | EPC code length，default :12 |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation:

This deduction operation is irreversible. To avoid the mis-operation to other tags, an attached EPC code field should be added to the instruction. Only after reader getting the matching EPC code from the tag then the operation can be executed. If there is no added field destruction order will be executed without identification.

EPC code length has difference according to different signal tag. Default value is 12 bits.

The default password is "00000000", but according to the protocol the password must be changed before destruction operation.

5.15  EAS Bit zone setting

| Description | This function is used to set the EAS bit zone. |
| --- | --- |
| Prototype | bool UHF_6CEASFlagSet(void *pHandle, unsigned char nAntenna, unsigned char nType, unsigned char* pAccessPwd, int nEASFlag) |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | the antenna port number when operating tags(1-4) |
|  | nType | ESA Setting operation mode |
|  | pAccessPwd | tag visiting password |
|  | nEASFlag | EAS Bit zone setting |
|  |  | 0 cancel EAS Bit zone 1 set EAS Bit zone |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

Explanation：

This function needs tags with this application, at present some tags of NXP support this function. Please ask supplier to get details.

5.16  Start EAS monitoring

| Description | This function is used to start or stop EAS monitoring function. |
| --- | --- |
| Prototype | bool UHF_6CEASMonitorEnable (void *pHandle, unsigned char nAntenna, unsigned char nSetEAS) Incoming Parameters: |
| Parameter | pHandle | the opening port handle |
|  | nAntenna | the antenna port number when operating tags(1-4) |
|  | nSetEAS | EAS monitoring operation control |
|  |  | 0x00 -> Read end the EAS monitoring operation 0x01 -> Read start the EAS monitoring operation |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

- API Setting

6.1  API Versions information inquiry

| Description | This function is used to inquire the current API function Versions information. |
| --- | --- |
| Prototype | bool UHF_Copyright (void *pHandle, char* copyright) |
| Parameter | pHandle | the opening port handle |
|  | copyright | versions information |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

6.2  Setting API trends library language type

| Description | This function is used to set API trends library language type. |
| --- | --- |
| Prototype | bool UHF_SetLanguageType(void *pHandle, char* szType) |
| Parameter | pHandle | the opening port handle |
|  | szType | language form |
|  |  | cn Simplified Chinese tw Chinese Traditional en English. |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

6.3  Get Error Message

| Description | This function is used to get returning error message from reader. |
| --- | --- |
| Prototype | bool UHF_GetErrorMessage(void *pHandle,char *szMsg, int nLen) |
| Parameter | pHandle | the opening port handle |
|  | szMsg | returning error message |
|  | nLen | szMsg buffer length |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

6.4  Get Error Code

| Description | This function is used to get returning error code from reader. |
| --- | --- |
| Prototype | bool UHF_GetErrorCode (void *pHandle,int *pCode); |
| Parameter | pHandle | the opening port handle |
|  | pCode | returning error code |
| Return | true | Operation Success; |
|  | false | Operation Failed. |

# Appendix A: Error code list

When executing order from upper computer failed, the reader will send back the error code and point out the operation failure reason.

Error code field is dividing as following:

| 0x10-0x1F | Reader system error code |
| --- | --- |
| 0x20-0x2F | Reader operation error code |
| 0x60-0x6F | Reader data transmission error code |
| 0xA0-0xAF | ISO18000-6B Tag operation error code |
| 0xB0-0xBF | ISO18000-6CTag operation error code |

Error code is definitely defined as below:

Table A-1 Reader system error code list

| Error code | Error code definition |
| --- | --- |
| 0x10 | Wrong software version in Reader decoding unit |
| 0x11 | Wrong hardware in Reader base band board |
| 0x12 | Wrong hardware in Reader RF board |
| 0x13 | Self-checking error in reader system parameter list |
| 0x14 | Self-checking error in Reader base band board |
| 0x15 | Self-checking error in Reader RF board |
| 0x16 | Ethernet Detection error in Reader |
| 0x17 | RTC Detection error in Reader |
| 0x18 | External Rom detection in Reader |
| 0x19 | Retain |
| 0x1A | Retain |
| 0x1B | Retain |
| 0x1C | Retain |
| 0x1D | Retain |
| 0x1E | Retain |
| 0x1F | Unknown system error code |

Table A-2 Reader operation error code list

| Error code | Error code definition |
| --- | --- |
| 0x20 | Operation password error |
| 0x21 | Using wrong antenna port number |
| 0x22 | Reader currently in testing mode |
| 0x23 | Get data in Reader internal storage device is failure |
| 0x24 | The Reader is Currently operating the tag |
| 0x25 | Run-time error, such as illegal operation in program run |
| 0x26 | Operation rights is blocked（Someone else has connected and used the Reader ） |
| 0x27 | Retain |
| 0x28 | Retain |
| 0x29 | Retain |
| 0x2A | Retain |
| 0x2B | Retain |
| 0x2C | Retain |
| 0x2D | Retain |
| 0x2E | Retain |
| 0x2F | Unknown Reader operation error |

Table A-3 Data transmission error code list

| Error code | Error code definition |
| --- | --- |
| 0x60 | Imperfect frames in Received instruction or data |
| 0x61 | CRC error in Received instruction or data |
| 0x62 | The current Reader cannot support this type the instruction |
| 0x63 | The current Reader cannot support the tag protocol |
| 0x64 | Parameter error in instruction |
| 0x65 | Instruction frames error（lack of domain or structure error in domain) |
| 0x66 | Cannot support this kind of instruction |
| 0x67 | Read receive too much instruction, and cannot handle temporarily |
| 0x68 | Retain |
| 0x69 | Retain |
| 0x6A | Retain |
| 0x6B | Retain |
| 0x6C | Retain |
| 0x6D | Retain |
| 0x6E | Retain |
| 0x6F | Unknown data transmission error |

Table A-4 ISO18000-6B Tag operation error code list

| Error code | Error code definition |
| --- | --- |
| 0xA0 | No response or no tag within RF range |
| 0xA1 | Tag doesn't support the command |
| 0xA2 | The command is not identified by tag, or address error |
| 0xA3 | This option is not supported |
| 0xA4 | Unknown error returned by tag |
| 0xA5 | Tag can not access a particular bank |
| 0xA6 | Specified bytes of tag is locked, and can not be re-locked |
| 0xA7 | Specified bytes of tag is locked, and can not be re-written |
| 0xA8 | Tag executing bytes of data writing failed |
| 0xA9 | Tag executing bytes locking failed |
| 0xAA | Tag operation is cut down by host computer(such as carrier) |
| 0xAB | Tag operation is not fulfilled due to interfering or others reasons |
| 0xAC | Tag returns CRC error |
| 0xAD | Retain |
| 0xAE | Retain |
| 0xAF | Unknown ISO18000-6B type tag operation error |

Table A-5 ISO18000-6C Tag operation error code list

| Error code | Error code definition |
| --- | --- |
| 0xB0 | No response or no tag within RF range |
| 0xB1 | The target storage bank of tag doesn't exist |
| 0xB2 | Tag return information: address of tag operation overflowing |
| 0xB3 | Tag return information: operation storage bank is locked |
| 0xB4 | Tag access password error |
| 0xB5 | Tag deactivate password error |
| 0XB6 | Tag operation is cut down by host computer(such as carrier) |
| 0xB7 | The tag, which is for reading/writing/locking data bank, has not been initialized. |
| 0xB8 | Uninitialized tag is found |
| 0xB9 | Tag return information: unknown error |
| 0xBA | Tag return information: underpowered |
| 0xBB | Retain |
| 0xBC | Retain |
| 0xBD | Retain |
| 0xBE | Retain |
| 0xBF | Unknown ISO18000-6C type tag operation error |